Preflight Compete

| Before Starting Engine |
| --- |
| Seats & Belts | Adjusted & Locked |
| Brakes | Test & Set |
| Fuel Selector | Both |

| Starting Engine |
| --- |
| Radio Master | Off |
| Mixture | Rich |
| Carburetor Heat | Cold |
| Master Switch | On |
| Circuit Breakers | Check |
| Primer | 2 – 6 Strokes |
| Throttle | Pump 2 1/8 Open |
| Master Switch | ON |
| Propeller Area | Clear |
| Ignition Switch | START |
| Throttle Set | <1000 RPM |
| Oil Pressure | Check |

| Before Taxi |
| --- |
| Radios Master | On |
| Com & Nav | Set |
| Transponder | Standby |
| Nav Lights/Beacon | As Needed |
| Instrument w/ATIS | Set |
| Heading Indicator | Set to compass |
| Contact Ground | Intentions |
| Test Brakes | Check |

| Before Takeoff |
| --- |
| Aircraft Into Wind | Check |
| Parking Break | SET |
| Flight Controls | Free & Correct |
| Trim Tab | Takeoff Setting |
| Throttle | 1700 RPM |
| Engine Instruments | Check |
| Full Carburetor Heat | Check RPM Drop |
| Magnetos (50 rpm Max Difference – 125 Max Drop) | Check |
| Ammeter | Check |
| Suction Gage | (4.6 – 5.4 inches) |
| Throttle Full OUT | Check no stall |
| Return to Idle | <1000 RPM |
| Flight Instruments | Set |
| Radio & Intercom | Set |
| Wing Flaps | 0 normal & short/ 10 deg. soft –rough fields |
| Transponder | Altitude |
| Clearing Turn | Check |
| Cabin Doors/Windows | Latched & Locked |
| Contact Tower | Takeoff Clearance |
| Time of Takeoff | Noted |

##### HELENA FREQUENCIES

###### ATIS			 	120.40

GROUND		 	121.90

##### TOWER			118.30

# APPROACH			119.5

# UNICOM			122.95

GTF FSS         		122.55

VORTAC			117.70

| Normal Takeoff |
| --- |
| Wing Flaps | None |
| Carburetor Heat | Cold |
| Mixture | Lean above 3000 msl |
| Power | Full |
| Rotate | 60 mph |
| Climb Speed | 80 mph (Vy) |
| Adjust Trim | As Needed |
| MAX Performance Takeoff |
| Wing Flaps | 0 short field 10 deg. soft –rough fields |
| Carburetor Heat | Cold |
| Mixture | Lean above 3000 msl |
| Brakes | Apply |
| Power | Full |
| Brakes | Release |
| Attitude | Slight tail low |
| Rotate | 60 mph |
| Climb Speed to clear obstacles | 65/68 mph (Vx) 10/0 flaps |
| Raise Flaps Slowly | Obstacle clr. |
| Climb | 80-90 mph |
| Adjust Trim | As Needed |
| Cruise Climb |
| Power | Full |
| Speed | 80-90 normal 73-81 max performance |
| Mixture | Lean above 3000 msl |
| Adjust Trim | As Needed |
| Select Fuel Tank | As Needed |
| Cruise |
| Power (per altitude) 75% power above 5000 msl | 2600-2700 rpm |
| Mixture | As Needed |

| Descent |
| --- |
| Carburetor Heat | On |
| Power | As Needed |
| Adjust Trim | As Needed |
| Mixture | Rich |
| Before Landing |
| Fuel Selector Valve | Both |
| Mixture | Rich |
| Power | As Needed |
| Carburetor Heat | On |
| Wing Flaps | As Needed |
| Airspeed – Flaps Up – Flaps Down | 70 – 80 mph 65 – 75 mph |
| Safety Belts | Secure |
| Go Around |
| Power | Full |
| Carb Heat | Cold |
| Flaps | 20 |
| Speed | 65mph |
| Flaps | Retract slowly |

| Engine Failure |
| --- |
| Airspeed (Best Glide) | 80 mph Flaps Up |
| Select Landing Area | Into Wind Turn Toward Area |
| Restart Checklist | Check/Change Fuel Tank Mixture – Rich Magnetos – Both Primer – In & Locked |
| Communicate | Declare Emergency |
| Set Up | Landing / Approach |
| Restart Fails |
| Mixture | Idle / Cut-Off |
| Fuel Valve | Off |
| Ignition | Off |
| Switches | Off (Except Master) |
| Airspeed | 70 – 80 mph (Flaps Up) |
| Wing Flaps | Extend Only When Certain Extend As Necessary |
| Airspeed | 65 – 75 mph (Flaps Down) |
| Cabin Doors | Unlatched |
| Attitude | Slightly Tail Low |
| Upon Touchdown | Apply Heavy Brake Full Up Elevator |

# Text boxes

Fuel:		42 Gals. /38 Useable

- Shutdown –

Flaps                                           Up

Carb Heat                                  Cold

Avionics		             Off

Mixture			Full Lean

Throttle			Full In

Beacon/Lights			Off

Magnetos			Off

Master Switch			Off